## Slide 1: Introduction to ESP32 Microcontroller
Beginner’s Guide + Pinouts Overview

## Slide 2: What is ESP32?
• Low-cost, low-power microcontroller
• Built-in Wi-Fi + Bluetooth
• Multiple GPIO, ADC, DAC, PWM
• Ideal for IoT, robotics, embedded projects

## Slide 3: ESP32 Features
• Dual-core 32-bit processor
• 520 KB SRAM, up to 16 MB Flash
• 34 GPIO pins
• ADC (18 channels, 12-bit)
• 2 × DAC, PWM on all pins
• UART, I2C, SPI support

## Slide 4: ESP32 Development Boards
• ESP32-WROOM-32 (most common)
• ESP32 DevKit v1 (NodeMCU-32S)
• ESP32-S2, ESP32-C3, ESP32-S3

## Slide 5: Setting Up ESP32
• Install Arduino IDE
• Add ESP32 boards via Board Manager URL
• Select board (ESP32 Dev Module)
• Connect with USB cable

## Slide 6: First Program – Blink LED
int led = 2;
void setup() {
pinMode(led, OUTPUT);
}
void loop() {
digitalWrite(led, HIGH); delay(1000);
digitalWrite(led, LOW); delay(1000);
}

## Slide 7: ESP32 Pinout Overview
• Power pins (3.3V, GND, VIN)
• Digital I/O pins
• ADC & DAC pins
• Communication pins (UART, I2C, SPI)
• Special boot pins

## Slide 8: GPIO Usage Tips
• Avoid GPIO 6–11 (used for flash)
• Bootstrapping pins: GPIO 0, 2, 15
• Safe GPIOs: 4, 5, 18, 19, 21–23, 25–27, 32–39

## Slide 9: Summary
• ESP32 = powerful + versatile MCU
• Supports Wi-Fi, Bluetooth, ADC, DAC, PWM
• Great for IoT and embedded projects
• Easy to program with Arduino IDE